## Slide 1: Doggy, the TJBot’s companion
When AI meets pets

## Slide 2: Learning Objectives
This activity complement “What’s Possible With AI – TJ Bot” Activity Kit expanding students’ knowledge regarding robotics , cognitive technologies and AI by helping them build a simple companion for TJBot, a cute dog called Doggy. Students will increase experience and skill using a Raspberry Pi, Servo Motors, Sonar sensor and unleash their creativity following TJBot and Doggy in funny tales powered by Watson™ services.
Audience:
  Ages 11-14 (Middle grade students)
  Ages 14-19 (Secondary/high school students)
What’s the goal of this kit?
  Introduce cognitive technologies and programming
  Explore “embedded cognition”— everyday objects that use AI to interact with us
  Support environmental education activity reusing cardboard and common material
Why is this topic important?
  The technologies introduced through this activity have a growing impact in our world.
  A fun, creative, hands-on project is an ideal way to stimulate students’ interest in STEM topics
Hint: Remove this slide from student presentation

## Slide 3: Activity Kit structure and generic requirements
This activity is composed by tales and scenes, with clear requirements and detailed steps.
Common requirements:
TJBot already setup and tested with Node-Red nodes by JeanCarl Bisson
Doggy already setup and tested (note: some scenes require a specific Doggy version. Build your Doggy according to the story that you want to tell). This activity also includes instructions to build Doggy.
Skill: Node-Red (basic level)
Age: 8+ (Doggy already setup and tested)
Age: 12+ (Doggy not yet built and setup)
Before starting, verify if updates, including more tales, are available on Doggy Web Site
Hint: Remove this slide from student presentation

## Slide 4: What are we going to do today?
TJBot loves pets even though they can be noisy. He/Her owns two dogs, Doggy and MiniDoggy.
Doggy is a very careful watchdog while MiniDoggy is more distracted one, it doesn’t look at what happens around it but it’s happy to play with TJBot.
We follow TJBot and its doggies in some funny stories learning how IBM solutions could be applied to real life examples.
Doggy is an original idea from IBM Italy Volunteers. The first draft version was developed during a stage with high school students in IBM Italy Segrate, May 2018.

## Slide 5: Detailed Agenda (click & go)
Create and setup your own Doggy (Doggy Basic, Doggy Standard, Doggy Premium, MiniDoggy)
Tale 1 - Nothing and no one can pass without getting a strong barking from Doggy. TJBot calms it, getting a cute tail wagging from Doggy.
  Tale1.Scene1 - Create a flow that makes Doggy say “BARK!” if an object is less than 30cm away
  Tale1.Scene2 – Make Doggy barking (a real barking!) if an object is less than 30cm away
  Tale1.Scene3 – Smart barking, just one time, please!
  Tale1.Scene4 – Doggy is happy and wags its tail!
  Tale1.Scene5 - TJBot wakes up when Doggy start barking and calms it recognizing the object
Tale 2 – Doggy likes his treats. It needs to eat healthier and start doing exercises
  Tale2.Scene1 - Stand Up, Doggy - Doggy stands up on its front legs when anything is less that 30cm away
  Tale2.Scene2 – Doggy, trying to do push-ups - Doggy does push-ups when anything is less that 30cm away
  Tale2.Scene3 – TJBot helps Doggy doing exercises - When anything is less that 30cm away, TJBot start counting push-ups for Doggy

## Slide 6: Instruction: Create and setup your own Doggy
Doggy's family:
DOGGY BASIC - Doggy hosts an HC-SR04 sensor that provides a superdog vision.
DOGGY STANDARD - In addition to BASIC format, Doggy has also a very cute tail, powered by one SG-90 servo motor.
DOGGY ADVANCED (PREMIUM) - Doggy increases its capability with two motorized front legs powered by 2 x SG-90 servo motors.
MINIDOGGY - This little Doggy has just a tail moved by one SG-90 servo motor. Little and very friendly!
Doggy is very easy to build because it’s provided with A4 format design file (DXF/PDF). Just print/copy it and cut, fold, connect!
Agenda
Before let Doggy runs through digital fields, we have to test its features and tune up some little things. Apply the following setup instructions to your Doggy version:
Setup and Test Doggy superdog vision (HC-SR04)
Setup and Test Doggy tail (SG-90)
Setup and Test Doggy front legs (SG-90)
Level: some tasks could be tricky but could be performed under adult’s guidance

## Slide 7: HW requirement
Level: some tasks could be tricky but could be performed under adult’s guidance
Agenda
Component | Doggy Basic | Doggy Standard | Doggy Advanced (Premium) | MiniDoggy
TJBot setup with JCBisson Node-Red nodes | Yes | Yes | Yes | Yes
1 x HC-SR04 ultrasonic sensor for TJDog supervision | Yes | Yes | Yes | No
1 x SG90 servo motor for TJDog tail | No | Yes | Yes | Yes
2 x SG90 servo motor for TJDog front legs | No | No | Yes | No
1 x Breadboard | No | Optional | Yes | No
Cables, Cardboard, stapler, marking pens, scotch tape | Yes | Yes | Yes | Yes
Instruction: Create your own Doggy – 2

## Slide 8: Download and Print/Copy Design files
Get the last design file from Doggy Github house
Doggy Basic - Superdog vision only (Doggy DXF format, Doggy PDF format - basic parts)
Doggy Standard - Basic plus ultra-dynamic tail (Doggy DXF format, Doggy PDF format - basic parts
Doggy Premium - Standard plus powerful front legs (Doggy DXF format, Doggy PDF format - basic parts, Doggy PDF format - Optional and advanced parts)
MiniDoggy - ultra-dynamic tail only (MiniDoggy DXF format, MiniDoggy PDF format)
Agenda
Level: some tasks could be tricky but could be performed under adult’s guidance
Print or Copy the design file on selected support
Doggy Basic - Do not use common printer paper. Doggy Basic can be easily printed on 200gr/m² A4 paper (local print shop or standard printer) or cardboard. 200gr/m² A4 paper is enough strong to support sensor weight. No need for "Belly" part (but if you like it, just fold and insert it).
Doggy Standard – As Basic, "Belly" part is optional, depending upon wiring choices (but if you like it, just fold and insert it).
Doggy Premium – As Basic, except that "Belly" part is mandatory. It could be printed on 200gr/m² A4 paper, but cardboard is the best choice.
MiniDoggy - MiniDoggy can be easily printed on 200gr/m² A4 paper (local print shop or standard printer) 200gr/m² A4 paper is enough strong to support servo motor weight. No need for "Belly" part (but if you like it, just fold it and insert mounting servo on it). Belly part is mandatory if you use standard printer paper.
Please, share your experience on Doggy's House!!!
HINT: The best way to learn how to build Doggy is to print it on common A4 paper and build a prototype.
Instruction: Create your own Doggy – 3

## Slide 9: Mount Doggy Basic - a TJBot companion with superdog vision!
Agenda
fold up or down cyan and green lines
Instruction: Create your own Doggy – 4a
Get and Print/Copy DOGGY BASIC design file - Print/reproduce only the Tail and advanced Sheet
Cut all the red lines using a cutter and a scissor (do not cut parts to host servo motor for tail). If you plan to use superdog vision, remind to cut eyes too. (P.S: in the following pictures these lines are cut as used in Standard and Advanced version)
fold up
fold down

## Slide 10: Mount Doggy Basic - a TJBot companion with superdog vision!
Agenda
Doggy is folded up & down (and I forget to cut eyes  )
Instruction: Create your own Doggy – 4b
staple neck and back (this phot is from the Standard - Premium Doggy)
staple left and right ears
insert tongue and clip the tail

## Slide 11: Mount Doggy Basic - a TJBot companion with superdog vision!
Agenda
Insert and wire HC-SR04 sensor to TJBot (no need for breadboard).
Build a leash keeping connectors together… or you can braid them 
WARNING: pay attention to connect the right PINs to avoid damages to components.
Please, share your experience on Doggy's House!!!
Instruction: Create your own Doggy – 4c
Description | From TJBot to Doggy’s eyes
Type of connectors | Female to Female
Pin 25 - Ground | Blue to Ground
Pin 23 - GPIO 11 - Echo | Green to Echo
Pin 21 - GPIO 09 - Trigger | Yellow to Trigger
Pin 4 - 5V | Orange to VCC
Enjoy your Doggy Basic

## Slide 12: Mount Doggy Standard - a TJBot companion with superdog vision and a cute tail!
Agenda
fold up or down cyan and green lines
Instruction: Create your own Doggy – 5a
Get and Print/Copy DOGGY STANDARD design file - Print/reproduce only the Tail and advanced Sheet
Cut all the red lines using a cutter and a scissor. If you plan to use superdog vision, remind to cut eyes too.
fold up
fold down

## Slide 13: Mount Doggy Standard - a TJBot companion with superdog vision and a cute tail!
Agenda
Doggy is folded up & down (and I forget to cut eyes  )
Instruction: Create your own Doggy – 5b
staple neck and back
staple left and right ears
insert tongue and mount servo motor as shown in figure
(if you forget to cut eyes, remove it and insert HC-SR04 sensor)

## Slide 14: Mount Doggy Standard - a TJBot companion with superdog vision and a cute tail!
Agenda
Wire HC-SR04 sensor and SG-90 servo motor to TJBot (look at the picture to insert servo with the right orientation). A breadboard could make this task easier, but it’s not strictly required.: fix breadboard to Doggy’s back (upside down).
Build a leash keeping connectors together… or you can braid them 
WARNING: pay attention to connect the right PINs to avoid damages to components.
Instruction: Create your own Doggy – 5c
Description | From TJBot | From Doggy’s eyes | From Doggy’s tail
Type of connectors | Female to Male | Male to Female | Male to Male
Pin 25 - Ground | Blue | Blue to Ground | Brown to Brown (Ground)
Pin 23 - GPIO 11 - Echo | Violet | Green to Echo | 
Pin 21 - GPIO 09 - Trigger | Gray | Yellow to Trigger | 
Pin 4 - 5V White | Orange to VCC | Red to Red (5V) | 
Pin 24 - GPIO 08 Data servo motor (tail) | Black | Orange to Orange (Data servo motor) | 
WARNING: Using Doggy, TJBot is requiring more power than usual. Power it with 2.4A and everything will be fine!

## Slide 15: Mount Doggy Standard - a TJBot companion with superdog vision and a cute tail!
Agenda
Please, share your experience on Doggy's House!!!
Instruction: Create your own Doggy – 5d
Enjoy your Doggy Standard
Build tail (version #1). Get Servo arm and tape tail to it.
Build tail (version #2).
Tail is a personality trait. Use your imagination and try different tails. In the following photo, I wrapped tail starting from servo arm to tail’s end creating a rotation effect.
(optional) - print and cut standard belly component from Optional/Advanced Parts design sheet

## Slide 16: Mount Doggy Premium - a TJBot companion with superdog vision, a cute tail and two legs!
Agenda
Instruction: Create your own Doggy – 6a
Get and Print/Copy DOGGY Premium design files
Cut and fold as described for previous Doggy’s versions.

## Slide 17: Mount Doggy Premium - a TJBot companion with superdog vision, a cute tail and two legs!
Agenda
Clip hind legs
Instruction: Create your own Doggy – 6b
Mount servo motors for front legs and clip to fix them
(optional and in beta version) If you want to tighten up belly component (e.g. if you print it on 200gr/m² A4 paper), print, cut, fold and clip the beam component

## Slide 18: Mount Doggy Premium - a TJBot companion with superdog vision, a cute tail and two legs!
Agenda
Please, share your experience on Doggy's House!!!
Instruction: Create your own Doggy – 6c
Cut and Roll up front legs on shortest side. TIP: Fix leg to servo arm as shown in picture, leaving space to attach it to servo and fixing leg to the external part. As tail, legs are personality traits. Use your imagination and try different legs. In the following photo, I wrapped legs starting from servo arm to leg’s end.
Wire HC-SR04 sensor and SG-90 servo motor (tail, right leg/arm, left leg/arm) to TJBot.
A breadboard is recommended. Fix breadboard to Doggy’s belly.
Build a leash keeping connectors together… or you can braid them 
WARNING: pay attention to connect the right PINs to avoid damages to components.
Description | From TJBot | From Doggy’s eyes | From Doggy’s tail | From Doggy’s left arm | From Doggy’s Right arm
Type of connectors | Female to Male | Male to Female | Male to Male | Male to Male | Male to Male
Pin 38 - GPIO 20 - Data servo motor (right Doggy’s arm) | Green |  |  |  | Violet to Orange (data servo motor)
Pin 40 - GPIO 21 - Data servo motor (left Doggy’s arm) | Yellow |  |  | Violet to Orange (data servo motor) | 
Pin 25 - Ground | Blue | Blue to Ground | Brown to Brown (Ground) | Brown to Brown (Ground) | Brown to Brown (Ground)
Pin 23 - GPIO 11 - Echo | Violet | Green to Echo |  |  | 
Pin 21 - GPIO 09 - Trigger | Gray | Yellow to Trigger |  |  | 
Pin 4 - 5V | White | Orange to VCC | Red to Red (5V) | Red to Red (5V) | Red to Red (5V)
Pin 24 - GPIO 08 - Data servo motor (tail) | Black |  | Orange to Orange (Data servo motor) |  | 

## Slide 19: Mount MiniDoggy – the cutest tail in TJworld
Agenda
Instruction: Create your own Doggy – 7a
fold up or down green and green lines
Get and Print/Copy MiniDoggy design file and Cut all the red lines using a cutter and a scissor.
staple ears
Staple neck and back; mount servo motor (simplest version)
mount servo motor (extended version)
(optional) If you like, or if you printed MiniDoggy on standard printer paper, fold and mount MiniDoggy's belly

## Slide 20: Mount MiniDoggy – the cutest tail in TJworld
Agenda
Instruction: Create your own Doggy – 7b
wire servo to TJBot (no need for breadboard)
Description | From TJBot | From MiniDoggy’s tail
Type of connectors | Female to Male | Male to Male
Pin 25 - Ground | Blue | Violet to Brown (Ground)
Pin 4 - 5V | White | Red to Red (5V)
Pin 24 - GPIO 08 - Data servo motor (tail) | Black | Yellow to Orange (Data servo motor)
insert tongue and enjoy your MiniDoggy
Build tail (version #1). Get Servo arm and tape tail to it.
Build tail (version #2). Tail is a personality trait. Use your imagination and try different tails. In the following photo, I wrapped tail starting from servo arm to tail’s end creating a rotation effect that I like.

## Slide 21: Instruction: Setup and test Doggy
First of all, if you never setup Node-Red environment on TJbot, follow JCBisson Node-Red nodes for TJBot - setup instructions.
Everything ok? Excellent! You can already follow other TJBot labs provided in TJBot Playbook GitHub space!
But... we want a Doggy!!!
Before let it run through digital fields, we have to test its features and tune up some little things.
Apply the following setup instructions to your version:
Setup and Test Doggy superdog vision (HC-SR04)
Setup and Test Doggy tail (SG-90)
Setup and Test Doggy front legs (SG-90)
Agenda
Instruction: Setup and test Doggy - 8

## Slide 22: Instruction: Setup and Test Doggy superdog vision (HC-SR04)
Doggy is a superdog! It has a supervision powered by a very easy to use sensor named HC-SR04. This is a ultrasonic sonar. It emits a sound that travels through the air. If there is an object on its path, the sound will bounce back to the sensor that evaluate travel time to calculate how far is the object. HC-SR04 is able to detect object from 2cm to 400cm (1” to 13 feet). Using HC-SR04 in Node-Red is very easy!
Agenda
Apply to: Doggy Basic, Doggy Standard, Doggy Premium
Instruction: Setup and test Doggy vision – 9a
point your browser to Node-Red URL - http://«TJBot_ip_address»:1880 and verify that TJBot and Node-red are fully functional
install node-red-node-pisrf node to manage HC-SR04 and superdog vision.
open Node-Red Dashboard.
click on Menu
select MANAGE PALETTE
choose INSTALL tab
search package inserting "pisrf" test in search field
push INSTALL button and wait successful installation.
press CLOSE to return to Node-Red dashboard.
Follow wiring instructions for your Doggy version. Note: If you've changed PINs connections, modify the example according to your layout.

## Slide 23: Instruction: Setup and Test Doggy superdog vision (HC-SR04)
Test superdog vision creating the following flow using RPI-SRF and DEBUG nodes
drag RPI-SRF node to working area; drag DEBUG node, too. Connect RPI-SRF to DEBUG.
double-click RPI-SRF node and configure it as shown in picture on the right.
push DEPLOY button and verify that in the DEBUG area you'll get the distance (in centimetres) between Doggy's head and an obstacle.
Agenda
Apply to: Doggy Basic, Doggy Standard, Doggy Premium
Instruction: Setup and test Doggy vision – 9b
That’s all! We’re ready to build a story with Doggy's superdog eyes!

## Slide 24: Instruction: Setup and Test Doggy tail (SG-90)
Doggy is a cute dog! It has tail that wags to show its happiness. A little servo motor (SG-90) moves the tail. Using SG-90 in Node-Red is very easy! Follow wiring instructions for your Doggy version.
Note: If you've changed PINs connections, modify the example according to your layout.
Apply to: MiniDoggy, Doggy Standard, Doggy Premium
Instruction: Setup and test Doggy tail – 10a
point your browser to Node-Red URL - http://«TJBot_ip_address»:1880 and verify that TJBot and Node-red are fully functional
install node-red-node-pi-gpiod node to manage SG-90 servo motor.
open Node-Red Dashboard.
click on Menu
select MANAGE PALETTE
choose INSTALL tab
search package inserting "pigpiod" test in search field
push INSTALL button and wait successful installation.
press CLOSE to return to Node-Red dashboard.
Agenda

## Slide 25: Instruction: Setup and Test Doggy tail (SG-90)
Agenda
Apply to: MiniDoggy, Doggy Standard, Doggy Premium
Instruction: Setup and test Doggy tail – 10b
take away Doggy's tail. We have to set the right position to avoid damages to it.
tune tail position creating the following flow using PI-GPIOD and INJECT nodes dragging three times INJECT node to working area (you'll get three nodes); drag PI-GPIOD node, too. Connect INJECT nodes to PI-GPIOD.
double-click the first INJECT node and configure it as shown in the following picture. It changes name to "Set TAIL to CENTER“
as previous step, configure other INJECT nodes with 0 and 100 integer value. New names will be "Set TAIL to RIGHT" and "Set TAIL to LEFT".
double-click PI-GPIOD node and configure it as shown in picture.
push DEPLOY button.
Push "Set TAIL to CENTER" inject node. Servo motor should reach middle position. Attach tail to Doggy in RAISED position.
Push "Set TAIL to LEFT" inject node. Does tail go to Doggy's left side? If not, verify that servo is mounted according with your Doggy's version.
Push "Set TAIL to RIGHT" inject node. Does tail go to Doggy's right side? If not, verify that servo is mounted according with your Doggy's version.
That’s all! We’re ready to build a story with Doggy’s cute tail!

## Slide 26: Instruction: Setup and Test Doggy front legs (SG-90)
Doggy Premium is a strong dog! It can raise up on its front legs to intimidate unknown object and people. Two little servo motors (SG-90) powers front legs. Follow wiring instructions for your Doggy version.
Note: If you've changed PINs connections, modify the example according to your layout.
Prerequisite: install node-red-node-pi-gpiod as described in previous slide
Apply to: Doggy Premium
Instruction: Setup and test Doggy front legs – 11a
point your browser to Node-Red URL - http://«TJBot_ip_address»:1880 and verify that TJBot and Node-red are fully functional
take away Doggy's legs. We have to set the right position to avoid damages to them.
Agenda
tune legs position creating the following flow using PI-GPIOD and INJECT nodes dragging four times INJECT node to working area (you'll get four nodes); drag twice PI-GPIOD node, too (You'll get two nodes). Connect two INJECT nodes per PI-GPIOD.

## Slide 27: Instruction: Setup and Test Doggy front legs (SG-90)
Apply to: Doggy Premium
Instruction: Setup and test Doggy front legs – 11b
double-click the first INJECT node and configure it as shown in picture. It changes name to "Set DOGGY LEFT ARM to DOWN“.
Agenda
Node | Name | Value
Inject #2 | Set DOGGY LEFT ARM to UP | 0
Inject #3 | Set DOGGY RIGHT ARM to DOWN | 0
Inject #4 | Set DOGGY RIGHT ARM to UP | 100
double-click PI-GPIOD nodes and configure them as shown in following pictures and push DEPLOY button.
configure other INJECT nodes as in following table

## Slide 28: Instruction: Setup and Test Doggy front legs (SG-90)
Apply to: Doggy Premium
Instruction: Setup and test Doggy front legs – 11c
Agenda
Push "Set DOGGY LEFT ARM to UP" and "Set DOGGY RIGHT ARM to UP" inject nodes. Attach front legs to let Doggy to its belly.
Push "Set DOGGY LEFT ARM to DOWN" and "Set DOGGY RIGHT ARM to DOWN" inject nodes. Does DOGGY raised up? If not, verify that servos are mounted as described in provided instructions.
That’s all! We’re ready to build a story with Doggy’s front legs!

## Slide 29: Tales of two Doggies
TJBot loves pets even they could be noisy. He/Her owns two dogs, Doggy and MiniDoggy.
Doggy is a very careful watchdog. Nothing and no one can pass in front of it without getting a strong barking.
Mini Doggy is more distracted one, it doesn’t look at what happens around it but it’s happy to play with TJBot.
In the following scenarios, we follow TJBot and its doggies in some funny stories learning how IBM solutions could be applied to real life examples.
Every tale includes Doggy requirement, Skills, Age, Knowledge acquired and preparation steps.
Tales available:
  Doggy barks and wags its tail if an object is less than 30cm away
  Doggy is a greedy pet and needs to eat better and exercise
Once upon a time…
We Need You!
Submit your stories to expand Doggy's behaviour :)

## Slide 30: Instruction: Tale 1 - Nothing and no one can pass without getting a strong barking from Doggy. TJBot calms it getting a cute tail wagging.
Tale1.Scene1 - Create a flow that makes Doggy say “BARK!” if an object is less than 30cm away
Tale1.Scene2 – Make Doggy barking (a real barking!) if an object is less than 30cm away
Tale1.Scene3 – Smart barking, just one time, please!
Tale1.Scene4 – Doggy is happy and wags its tail
Tale1.Scene5 - TJBot wakes up when Doggy start barking and calms it recognizing the object
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Challenges included

## Slide 31: Instruction: Tale1.Scene1 - Doggy say “BARK!” if an object is less than 30cm away
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy says “BARK!” T01S01a
Doggy is a very careful watchdog. Nothing and no one can pass without getting a strong barking.
Requirement: TJBot, Doggy (Basic, Standard or Premium) – already setup and tested
Skill: Node-Red (basic level)
Age: 8+
Knowledge acquired: Sonar sensor usage, test condition, set value to variable, debugging
Preparation steps (usually performed by IBMers, Teachers…):
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected.
  disable every existing Flow (double-click each label, set Status to “Disabled”, press “Done” to close)
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
create a new Flow
double-click Flow label and rename it to “Tale1.Scene1”. Press “Done” to close.
drag PI-SRF node to the working area
double-click PI-SRF node and configure it as shown in the following picture

## Slide 32: Instruction: Tale1.Scene1 - Doggy say “BARK!” if an object is less than 30cm away
Agenda
Instruction: Doggy says “BARK!” T01S01b
drag a SWITCH node to the working area
double-click SWITCH node and configure it as shown in the following picture
drag a line from the output of the first node to the input of the second one

## Slide 33: Instruction: Tale1.Scene1 - Doggy say “BARK!” if an object is less than 30cm away
Agenda
Instruction: Doggy says “BARK!” T01S01c
drag a CHANGE node to the working area
configure CHANGE node setting the message to “BARK!”
connect the first output from SWITCH node to the input of CHANGE one

## Slide 34: Instruction: Tale1.Scene1 - Doggy say “BARK!” if an object is less than 30cm away
Agenda
Instruction: Doggy says “BARK!” T01S01d
drag a DEBUG node to the working area
connect its input to the output of CHANGE node
press DEPLOY button and switch to “debug” tab (if not already highlighted)
What happen when you put an object near to Doggy’s eyes?
Excellent! But we want a strong bark not a text on dashboard.
We get it in the next scene!

## Slide 35: Instruction: Tale1.Scene2 –Doggy barks if an object is less than 30cm away
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy barks - T01S02a
Requirement: TJBot, Doggy (Basic, Standard or Premium) – already setup and tested
Skill: Node-Red (basic level)
Age: 8+
Knowledge acquired: Sonar sensor usage, test condition, set value to variable, debugging, play audio
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify that Tale1.Scene1 is enabled on dedicated Flow
  get a good sound file (WAV format) with a dog barking (e.g. dogbark2.wav)
  upload bark sound file to TJBot Desktop using VNC file transfer feature, an USB Key or whatever you like (e.g. /home/pi/Desktop/dogbark2.wav). P.S: You can download it directly using TJBot browser :D
  test TJBot speaker with bark audio file
point browser to Node-Red Dashboard http://«TJBot_ip_address»:1880
create a new Flow
double-click Flow label and rename it to “Tale1.Scene2”. Press “Done” to close.
double-click “Tale1.Scene1” Flow label and set status to “Disabled”. Press “Done” to close.
select all nodes in “Tale1.Scene1” Flow drawing an area over them
press CTRL+C keys to copy.

## Slide 36: Instruction: Tale1.Scene2 –Doggy barks if an object is less than 30cm away
Agenda
Instruction: Doggy barks - T01S02b
click on “Tale1.Scene2” Flow label
press CTRL+V keys to paste nodes. When you find the best place to paste them, right click to save positions.
delete DEBUG node (click on it and press DEL key)
double-click SWITCH node and modify it as shown in the following picture
drag SPEAK node (from TJBot palette) to the Working area

## Slide 37: Instruction: Tale1.Scene2 –Doggy barks if an object is less than 30cm away
Agenda
Instruction: Doggy barks - T01S02c
double-click SPEAK node, select BOT according to your environment, set MODE to “Play” and set NAME to “Bark”
connect it to CHANGE node and press DEPLOY button
Do you get a strong barking when you put an object near to Doggy’s eyes? If not, verify prerequisites (e.g. audio power turned on…)
What happen if the object stays near Doggy?
Congratulation! You’re ready to move to the next level! Let’s make Doggy a little smarter!

## Slide 38: Instruction: Tale1.Scene3 – Smart barking, just one time, please!
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy smart barks - T01S03a
Requirement: TJBot, Doggy (Basic, Standard or Premium) – already setup and tested
Skill: Node-Red (basic level)
Age: 8+
Knowledge acquired: Sonar sensor usage, test condition, set value to variable, debugging, play audio, use global variables
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify that Tale1.Scene2 is enabled on dedicated Flow
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
create a new Flow
double-click Flow label and rename it to “Tale1.Scene3”. Press “Done” to close.
double-click “Tale1.Scene2” Flow label and set status to “Disabled”. Press “Done” to close.
select all nodes in “Tale1.Scene2” Flow drawing an area over them
press CTRL+C keys to copy.
click on “Tale1.Scene3” Flow label
press CTRL+V keys to paste nodes. When you find the best place to paste them, right click to save positions.
delete connection between SWITCH and CHANGE nodes, and make space in the flow

## Slide 39: Instruction: Tale1.Scene3 – Smart barking, just one time, please!
Agenda
Instruction: Doggy smart barks - T01S03b
drag twice CHANGE node to Working area. Drag SWITCH node, too.
double-click upper new CHANGE node and configure it as follow. Press “Done” to close.
double-click other new CHANGE node and configure it as the image on the right.

## Slide 40: Instruction: Tale1.Scene3 – Smart barking, just one time, please!
Agenda
Instruction: Doggy smart barks - T01S03c
double-click new SWITCH node and configure it as follow. Press “Done” to close.
*(if needed, rearrange nodes to make space and) connect as show in picture and press DEPLOY button
What happen when an obstacle reaches Doggy? As previously, Doggy start barking.
What happen if the object stays near Doggy?
What needs to happen to let Doggy barking again?
Awesome! Doggy is growing up smarter, step by step! It’s time to shake its tail!

## Slide 41: Instruction: Tale1.Scene4 –Doggy is happy and wags its tail!
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy shakes its tail- T01S04a
Requirement: TJBot, MiniDoggy or Doggy (Basic, Standard or Premium) – already setup and tested
Skill: Node-Red (basic level)
Age: 8+
Knowledge acquired: Servo motor and Sonar sensor usage, test condition, set value to variable, use random values, create loop
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify if LOOPTIMER is installed. If not, install node-red-contrib-looptimer via “Manage Palette”
  (Doggy version only) verify that Tale1.Scene3 is enabled and working on dedicated Flow
point your browser to Node-Red Dashboard and create a new Flow
double-click Flow label and rename it to “Tale1.Scene4”. Press “Done” to close.
(Doggy version only) double-click “Tale1.Scene3” Flow label and set status to “Disabled”. Press “Done” to close.
(Doggy version only) select “Doggy Eyes” and “Less than 30cm” nodes in “Tale1.Scene3” Flow. Press CTRL+C keys to copy them. Click on “Tale1.Scene4” Flow label. Press CTRL+V keys to paste them.
(MiniDoggy only) drag INJECT node to Working area. Double-click it and configure as in following picture

## Slide 42: Instruction: Tale1.Scene4 –Doggy is happy and wags its tail!
Agenda
Instruction: Doggy shakes its tail- T01S04b
(MiniDoggy only) drag RANDOM node to Working area. Double-click it and configure as in following picture. rearrange and connect nodes
drag LOOPTIMER node to Working area. Configure it to fire 30 times, every 0.2 seconds.

## Slide 43: Instruction: Tale1.Scene4 –Doggy is happy and wags its tail!
Agenda
Instruction: Doggy shakes its tail- T01S04c
drag RANDOM node to Working area. Configure it to send an integer between 0 and 100.
drag PI-GPIOD node to Working Area and configure it to PIN 24 (GPIO 8)

## Slide 44: Instruction: Tale1.Scene4 –Doggy is happy and wags its tail!
Agenda
Instruction: Doggy shakes its tail- T01S04d
connect and rearrange, if needed, as show in the following picture. Press DEPLOY button
(MiniDoggy version only)
What happens when you press “Simulated Doggy’s Eyes” INJECT node?
Why the tail shakes only some time and not always?
HINT: add a debug node to show “Simulated Distance Measurement” output. Call it “Distance” and press DEPLOY. Press again “Simulated Doggy’s Eyes” INJECT node
(Doggy version only)
What happen when an obstacle reaches Doggy?
What happen if the object stays near Doggy?
Fantastic! Doggy is growing up smarter, step by step!

## Slide 45: Challenge T1C1: Add scene3 elements to make Doggy barking and wagging tail when an object is closer than 30cm.
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Click to show “one of many” solution!!!
Do. Or do not. There is no try.

## Slide 46: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: TJBot wakes up and calm Doggy - T01S05a
Requirement: TJBot, MiniDoggy or Doggy (Basic, Standard or Premium) – already setup and tested
Skill: Node-Red (basic level)
Age: 10+
Knowledge acquired: Servo motor and Sonar sensor usage, test condition, set value to variable, TJBot capabilities (Text to Speech, Visual Recognition, Wave)
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify if LOOPTIMER is installed from previous Scenes. If not, install node-red-contrib-looptimer via “Manage Palette”
  (Doggy version only) verify that Tale1.Scene3 is enabled and working on dedicated Flow
There are several steps blocks in this scene according to Doggy version used
Steps (part 1):
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
create a new Flow
double-click Flow label and rename it to “Tale1.Scene5”.
Press “Done” to close.
disable any other active flow.
select all nodes in “Tale1.Scene3” Flow. Press CTRL+C keys to copy them.
Click on “Tale1.Scene5” Flow label. Press CTRL+V keys to paste them.
Remember to check TJBot credentials

## Slide 47: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05b
Steps (part 2 - optional - Doggy Premium only):
drag twice PI-GPIOD node to working area (you'll get two nodes)
double-click PI-GPIOD nodes and configure them as shown in pictures on the right.
duplicate PI_GPIOD nodes (copy and paste)
drag four times CHANGE node to working area and configure them as shown in picture following the table provided
Node | Name | Value
Change #1 | Set DOGGY LEFT ARM to DOWN | 100
Change #2 | Set DOGGY LEFT ARM to UP | 0
Change #3 | Set DOGGY RIGHT ARM to DOWN | 0
Change #4 | Set DOGGY RIGHT ARM to UP | 100

## Slide 48: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05c
Steps … continue (part 2 - opional - Doggy Premium only):
connect and rearrange, if needed, as show in the following picture.
press DEPLOY button.
Steps (part 3): Let's TJBot take on the stage!
drag once OUTPUT LINK node to working area beside SPEAK node
drag one INPUT LINK node to working area below the flow. Double-click it and name it "Doggy is barking"
double-click OUTPUT NODE and link it to "Doggy is barking"
What happens moving object in front of Doggy?
(HINT: use comment nodes - Things can grow up very fast and one comment can save your life)

## Slide 49: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05d
Steps… continue (part 3): Let's TJBot take on the stage!
drag TJBot's SEE and SPEAK, TEMPLATE (and DEBUG) nodes from Palette and connect them as in picture
configure SEE, SPEAK and TEMPLATE nodes as following
This is the code inserted in FUNCTION to copy and paste:
Calm down, Doggy. That's only a {{payload.0.class}} !

## Slide 50: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05e
Steps… continue (part 3): Let's TJBot take on the stage!
drag twice TJBot's SHINE node to Working area. Connect and configure them as shown in following picture.
press DEPLOY button.
What happens moving object in front of Doggy?
What happens if an object goes away and then back while TJBot is talking?
Probably you (or your students) noticed that Doggy and TJBot try to identify multiple objects mixing barking and speaking. This is bad.
(IBMers/Teachers hint: this is the same solution used in Tale2.Scene2 - look at it to get the details)

## Slide 51: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05f
Steps… continue (part 3): change flow as in following picture and retry (changed nodes are highlighted).
TJBot and Doggy are more realistic?

## Slide 52: Instruction: Tale1.Scene5 – TJBot wakes up when Doggy start barking and calms it down
Agenda
Instruction: TJBot wakes up and calm Doggy - T01S05g
Steps (part 4): Doggy is calmed and happy When Doggy is calm, it shakes its tail and go down on its belly.
modify flow as shown in the following figure (hint: copy nodes from previous flow)
What happen when an obstacle reaches Doggy?
What happen if the object stays away from Doggy?
What happen if the object stays in front of Doggy’s eyes?

## Slide 53: Instruction: Tale 2 – Doggy loves his treats. He needs to eat healthier and start doing exercises
Doggy is a sweet tooth. It loves treats, cakes and ice cream. Also likes hamburgers, chips, pizza and pasta!
It’s getting fat, so it needs to eat healthier and start doing exercises! But it doesn’t like gymnastic!!!
Scene Index:
Tale2.Scene1 - Stand Up, Doggy - Doggy stands up on its front legs when anything is less that 30cm away
Tale2.Scene2 – Doggy, trying to do push-ups - Doggy does push-ups when anything is less that 30cm away
Tale2.Scene3 – TJBot helps Doggy doing its exercises - When anything is less that 30cm away, TJBot starts counting push-ups for Doggy
Agenda
Challenges included

## Slide 54: Instruction: Tale2.Scene1 –Doggy stands up on its front legs when anything is less that 30cm away
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy stand-up - T02S01a
Requirement: TJBot, Doggy Premium – already setup and tested
Skill: Node-Red (basic level)
Age: 8+
Knowledge acquired: Servo motor and Sonar sensor usage, test condition, set value to variable
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify that Tale1.Scene4 is enabled and working on dedicated Flow (or recreate it)
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880 and create a new Flow
double-click Flow label and rename it to “Tale1.Scene5”. Press “Done” to close.
double-click “Tale1.Scene4” Flow label and set status to “Disabled”. Press “Done” to close.
select “Doggy Eyes” and “Less than 30cm”nodes in “Tale1.Scene4” Flow. Press CTRL+C keys to copy them. Click on “Tale1.Scene5” Flow label. Press CTRL+V keys to paste them.
drag twice PI-GPIOD node to working area (you'll get two nodes)
double-click PI-GPIOD nodes and configure them as shown in following pictures.

## Slide 55: Instruction: Tale2.Scene1 –Doggy stands up on its front legs when anything is less that 30cm away
Agenda
Instruction: Doggy stand-up - T02S01b
drag four times CHANGE node to working area and configure them as shown in picture following the table provided
Node | Name | Value
Change #1 | Set DOGGY LEFT ARM to DOWN | 100
Change #2 | Set DOGGY LEFT ARM to UP | 0
Change #3 | Set DOGGY RIGHT ARM to DOWN | 0
Change #4 | Set DOGGY RIGHT ARM to UP | 100
connect and rearrange, if needed, as show in the following picture and press DEPLOY button
Anyone scared by Doggy? Don't panic! It's a cute dog.

## Slide 56: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02a
Requirement: TJBot, Doggy Premium – already setup and tested
Skill: Node-Red (basic level)
Age: 10+
Knowledge acquired: Servo motor and Sonar sensor usage, test condition, set value to variable, Node-red subflow, Problem decomposition
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify if LOOPTIMER is installed. If not, install node-red-contrib-looptimer via “Manage Palette”
  verify that Tale2.Scene1 is enabled and working on dedicated Flow
Steps (part 1 - just one push-up!):
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880 and create a new Flow. Rename it to “Subflow working area”. Press “Done” to close.
double-click “Tale2.Scene1” Flow label and set status to “Disabled”. Press “Done” to close.
select all nodes in “Tale2.Scene1” Flow. Press CTRL+C keys to copy them. Click on “Subflow working area” Flow label. Press CTRL+V keys to paste them.
select "Set Doggy LEFT ARM DOWN", "Set Doggy RIGHT ARM DOWN", "TJDog LEFT ARM Pin38" and "TJDog RIGHT ARM Pin40" nodes keeping CTRL key pressed.
Copy them on the same flow and select them
Click on Node-Red Menu, click on SUBFLOWS, and select "Selection to SubFlow". Selection will be substituted by a new node, that appears even in palette area.
Level: some task could be tricky but could be performed under adult’s guidance

## Slide 57: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02b
Steps (part 1… continue):
double-click on created subflow in the Palette area. It opens in Working area and could be edited. Click on value "1" in Inputs selector and connect new input node to CHANGE nodes
click on "Edit Properties" and change name to "Doggy Stand-Up". Press "Done" to close and close subflow editor.
do the same again with "Set Doggy LEFT ARM UP", "Set Doggy RIGHT ARM UP", "TJDog LEFT ARM Pin38" and "TJDog RIGHT ARM Pin40", creating a new subflow called "Doggy Sit Down". In the same way, you can create basic Doggy actions (shake.tail, bark...).
delete “Subflow working area” flow

## Slide 58: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02c
Steps (part 1… continue):
create a new Flow
double-click Flow label and rename it to “Tale2.Scene2”. Press “Done” to close.
double-click “Tale2.Scene1” Flow label.
select “Doggy Eyes” and “Less than 30cm”nodes in “Tale2.Scene1” Flow. Press CTRL+C keys to copy them. Click on “Tale2.Scene2” Flow label. Press CTRL+V keys to paste them.
OK, now start little, just one push-up! From palette, drag "Doggy Stand Up" and "Doggy Sit Down" subflows to Working area. Drag DELAY node, too. Double-click it and set a 1 second delay. Connect nodes as show in figure and press DEPLOY button
What happen when an obstacle reaches Doggy?
What happen if the object stays away from Doggy?
What happen if the object stays in front of Doggy’s eyes?
Doggy has to do more exercise :)

## Slide 59: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02d
Steps (part 2 - 10 push-ups):
create a subflow called "Doggy Push-Up" using "Doggy Stand Up", "Doggy Sit Down" and "delay 1s" nodes. Modify “Tale2.Scene2” flow using new created subflow.
drag once SWITCH node from Palette to Working area. Modify it as shown in figure
delete connection between SWITCH and "Doggy Push-Up"
drag once CHANGE node from Palette to Working area. Modify it as shown in figure

## Slide 60: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02e
Steps (part 2… continue):
drag another SWITCH node from Palette to Working area. Modify it as shown in figure
drag once FUNCTION node from Palette to Working area. Modify it as shown in figure, inserting the following code that set/increase pushups count:
drag once DELAY node from Palette to Working area. Set delay to 2 seconds.
Connect nodes as show in figure. Pay attention to create the loop!
`var myCount = flow.get("pushups") || 0;
myCount += 1;
flow.set("pushups", myCount);
return msg;`

## Slide 61: Instruction: Tale2.Scene2 –Doggy does push-ups when anything is less that 30cm away
Agenda
Instruction: Doggy does push-ups - T02S02f
Steps (part 2… continue):
we need to instantiate count variable (teacher/IBMers, introduce this concept to classroom). Drag once INJECT node to Working area and copy "reset push-up count" node. Configure INJECT node as shown and connect nodes. Press DEPLOY button
What happen when an obstacle reaches Doggy?
What happen if the object stays away from Doggy?
What happen if the object stays in front of Doggy’s eyes?

## Slide 62: Challenge T2C1: Doggy doesn't like to do exercises. When it start a series, if nothing is near to it, it moves its tail instead of doing push-ups.
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
In the next slides you can find one of many solution
Is there anybody?
Leisure time!!!

## Slide 63: Challenge T2C1: Doggy doesn't like to do exercises. When it start a series, if nothing is near to it, it moves its tail instead of doing push-ups.
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy is a lazy dog - T02C01a
Macro Steps:
save distance value
test if anything is near
create a new SubflowFlow called "Doggy Move Tail Right to Left" with DELAY, two change nodes and copied "TJdog Tail Pin24" from Doggy setup. Right tail position is at "0". Left is on "100" value.

## Slide 64: Challenge T2C1: Doggy doesn't like to do exercises. When it start a series, if nothing is near to it, it moves its tail instead of doing push-ups.
Agenda
Level: some task could be tricky but could be performed under adult’s guidance
Instruction: Doggy is a lazy dog - T02C01b
Macro Steps:
connect nodes as in following picture and deploy it.
What happen when you move an object in front of Doggy?

## Slide 65: Instruction: Tale2.Scene3 – TJBot helps Doggy doing exercises counting push-ups
Instruction: TJBot counts push-ups - T02S03a
Requirement: TJBot, Doggy Premium – already setup and tested
Skill: Node-Red (basic level)
Age: 10+
Knowledge acquired: Text to Speech, TJBot capabilities (wave, speak)
Preparation steps:
  point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880
  verify that TJBot is fully functional and node-red is working as expected (TJBot credentials, too).
  verify that Tale2.Scene2 is enabled and working on dedicated Flow
Steps (part 1 - TJBot speaks):
point your browser to Node-Red Dashboard - http://«TJBot_ip_address»:1880 and create a new Flow
double-click Flow label and rename it to “Tale2.Scene3”. Press “Done” to close.
double-click “Tale2.Scene2” Flow label and set status to “Disabled”. Press “Done” to close.
select all nodes in “Tale2.Scene2” Flow. Press CTRL+C keys to copy them. Click on “Tale2.Scene3” Flow label. Press CTRL+V keys to paste them.
drag FUNCTION node to Working area and modify it to create a message that include the current number of push-ups performed by Doggy. Code is provided for cut&paste 
Level: some task could be tricky but could be performed under adult’s guidance
var myCount = flow.get("pushups") || 0;
if (myCount < 10) {
msg.payload = myCount + "!";
}
else {
msg.payload = "Good job , Doggy!";
}
return msg;
Agenda

## Slide 66: Instruction: Tale2.Scene3 – TJBot helps Doggy doing exercises counting push-ups
Agenda
Instruction: TJBot counts push-ups - T02S03b
Steps (part 1 - continue):
drag TJBot's SPEAK node to Working area connecting it
configure TJBot's SPEAK node according with your TJBot configuration (TTS credential, HW setup...) and press DEPLOY
(Note for Teacher/IBMers: this is a good time to explain local vs central processing)
What happen when an obstacle reaches Doggy?
Is TJBot in synch with Doggy exercises?
How can we get TJBot and Doggy more synched?

## Slide 67: Instruction: Tale2.Scene3 – TJBot helps Doggy doing exercises counting push-ups
Agenda
Instruction: TJBot counts push-ups - T02S03c
Solution: connect Doggy subflow to a different node)
Challenge time: Now, leverage on TJBot capabilities. TJBot thinks that could be useful to move his/her arm while Doggy do push-ups and to light up led to advice that a new series is started.
Ready… Steady… Go!!!
(a candidate solution on next slide)

## Slide 68: Challenge T2C2: TJBot thinks that could be useful to move his/her arm while Doggy do push-ups and to light up led to advice that a new series is started.
Agenda
We Need You!
Submit your scenes to expand Doggy's behaviour :)

## Slide 69: End notes and Credits
TJBot is a brilliant way to introduce and play with IBM Watson solution and robotics.
Node-Red makes programming a very easy task, from children to grandparents.
Doggy shows how to expand TJBot using common and low cost IOT devices.
Mixing all together is an excellent way to have fun and effective activities.
Ferruccio Manclossi,
Segrate, September 2018
https://github.com/fmanclossi/TJBot-playbook
Doggy is an original idea from a team of IBM Italy Volunteers. The first draft was developed during a stage with high school students in IBM Segrate, July 2018. A special GRAZIE to Fabrizio Repossi, Hossam Lemtaffah, Matteo Vergottini, Riccardo Manfredonia, Thierno Filippo D'Amelio and Usama Muhammad
“The goal of education is not to increase the amount of knowledge but to create the possibilities for a child to invent and discover, to create men who are capable of doing new things.”
Jean Piaget